## Slide 1: Using PTWC New Products for National Warnings and Evacuation Land Coastal Flooding, Marine Threats, and Public Safety
Brian Yanagi, Dr. Laura Kong
brian.yanagi@noaa.gov, laura.kong@noaa.gov
Dr. Charles McCreery
Director, US NOAA Pacific Tsunami Warning Center
charles.mccreery@noaa.gov
Notes: <number>
This presentation describes how National Disaster Management Organizations (NDMO) can interpret PTWC New Products for issuance of National Warnings and Evacuation. PTWC New Product tsunami wave forecasts will include Land Coastal Flooding and Marine Threats to be used to make Public Safety decisions.

## Slide 2: FORECAST => EMERGENCY RESPONSE
Amplitude > 3 m => Major Land Coastal Flooding Threat: Evacuate Tsunami Coastal Evacuation Zones
1 m ≤ Amplitude ≤ 3 m => Coastal Land Flooding Threat: Evacuate Tsunami Coastal Evacuation Zones
0.3 m ≤ Amplitude < 1 m => Marine Threat: Clear beaches, harbors, low lying coastal areas
Amplitude < 0.3 m => No Threat, No Evacuation
Value not computed => Monitor Event
Notes: The following are PTWC New Product forecasts and their associated Emergency Response actions. PTWC New Products will no longer have Warning / Watch threat assessments in their messages. Instead, National Tsunami Warning Centers (NTWC) are responsible for issuing Warning / Watch to their countries, based on maximum tsunami wave forecast amplitude measurements (from sea level to crest). Forecast amplitude > 3 meters means Major Land Coastal Flooding Threat, in which NDMOs should conduct a Full Scale Land Evacuation of their Tsunami Coastal Evacuation Zones. A forecast amplitude between 1 – 3 meters also poses a Coastal Land Flooding Threat, which NDMOs should similarly conduct a Full Scale Land Evacuation of their Tsunami Coastal Evacuation Zones. A forecast amplitude between 0.3 – 1 meter poses a Marine Threat due to strong currents. NDMOs should enable a clearing of persons from beaches and low lying coastal areas, and ocean deployment of ships from harbors, only if there is sufficient time to get underway before wave arrival. This is a precautionary action and NOT a Full Scale Land Evacuation. In the US, a “Tsunami Advisory” is issued for Marine Threat assessment due to strong and/or unsual currents. Forecast amplitude less than 0.3 meter means there is no threat and no need for evacuation. If forecast amplitudse have not been computed, the action is to monitor the event until a forecast is provided.
<number>

## Slide 3: Marine Threat
Santa Cruz, CA, USA
Chile tsunami, February 2010
Notes: The following photos depict the occurrence of strong tsunami currents and eddies from the December 2004 Indian Ocean tsunami off the coast of Sri Lanka, and the February 2010 Chile tsunami off the coast of Santa Cruz, California USA. Strong currents can cause boats to break their moorings. Wind waves and tsunami waves are generated differently. In a tsunami, an undersea earthquake displaces and transmits a huge amount of energy into the entire water column from the deep ocean floor to the sea surface. However, the tsunami wave amplitude in the deep water may be only a few centimeters high as it crosses the ocean basin. Wave heights grow in shallow water.
<number>

## Slide 4: Land Coastal Flooding Threat
New Zealand, Chile tsunami, February 2010
Notes: This New Zealand tsunami photo depicts a Land Coastal Flooding Threat (forecast amplitude between 1-3 meters) from the February 2010 Chile tsunami. NDMOs should enable a full scale land evacuation of its coastal tsunami evacuation zones.
<number>

## Slide 5: Major Land Coastal Flooding Threat
Sendai, Japan, Japan tsunami, March 2011
Notes: This photo from the March 2011 tsunami in Sendai, Japan depicts a Major Land Coastal Flooding Threat (forecast amplitude > 3 meters). NDMOs should enable a full scale land evacuation of its coastal tsunami evacuation zones.
<number>

## Slide 6: Alert Criteria Table OT + 10 min: No PTWC Forecast
Notes: Please see Appendices VI for more explanation:
Users Guide for the Pacific Tsunami Warning Center Enhanced Products for the Pacific Tsunami Warning System. IOC Technical Series No 105, Revised edition. UNESCO/IOC, 2014 (English; Spanish)
Available for download at http://ptws-ptwcnewproducts.info
<number>

## Slide 7: Alert Criteria Table OT + 30 min: Quantitative PTWC Forecast – 1 m
Notes: Please see Appendices VI for more explanation:
Users Guide for the Pacific Tsunami Warning Center Enhanced Products for the Pacific Tsunami Warning System. IOC Technical Series No 105, Revised edition. UNESCO/IOC, 2014 (English; Spanish)
Available for download at http://ptws-ptwcnewproducts.info
<number>

## Slide 8: Alert Criteria Table OT + 30 min: Quantitative PTWC Forecast – 0.3 / 1 m
Notes: Please see Appendices VI for more explanation:
Users Guide for the Pacific Tsunami Warning Center Enhanced Products for the Pacific Tsunami Warning System. IOC Technical Series No 105, Revised edition. UNESCO/IOC, 2014 (English; Spanish)
Available for download at http://ptws-ptwcnewproducts.info
<number>

## Slide 9: School Evacuation Drills
Annual – Every school in evacuation zone
Drill is Evacuation only
Coordinated by Ministry of Education, in cooperation with Emergency Management Agency
Notes: <number>
NTWCs and NDMOs are encouraged to conduct routine tsunami exercises within their countries to identify strengths and weaknesses in enabling their tsunami response Standard Operating Procedures. Exercises can range from a simple Orientation Workshop to a Full-Scale Exercise. IOC Manual and Guides 58 (rev 2013) How to Plan, Conduct and Evaluate UNESCO/IOC Tsunami Wave Exercises provides further information. If a country does not currently conduct tsunami exercises, it is recommended to start with annual school evacuation drills, coordinated through their Ministry of Education.

## Slide 10: Thank You
Brian Yanagi, Dr. Laura Kong
brian.yanagi@noaa.gov, laura.kong@noaa.gov
Dr. Charles McCreery
Director, US NOAA Pacific Tsunami Warning Center
charles.mccreery@noaa.gov
Notes: <number>