## Slide 1: Exercise Pacific Wave 2017 PacWave17 Overview
Laura Kong
International Tsunami Information Center
Jo Guard
New Zealand Ministry of Civil Defence & Emergency Management
Tomoaki Ozaki
Japan Meteorological Agency
Notes: <number>

## Slide 2: Exercise Pacific Wave (PacWave)
IOC-coordinated international tsunami exercises
Started 2006 to test readiness of Pacific countries – 2006, 2008, 2011, 2013, 2015, 2016, 2017
PacWave11, 13, 15 – introduce and test PTWC new enhanced products prior to changeover (1 October 2014), and after
PacWave 16, 17 - introduce and test JAM NWPTAC new enhanced products prior to changeover (2018)

## Slide 3: PacWave 16 and 17 – Overall Goals
  Test NWPTAC new products prior to implementation through 2 PacWave exercises
  PacWave16
  Small-scale exercise with 16 countries that receive NWPTAC products
  Table-top exercise recommended
  PacWave17
  Full-scale exercise with all Member States
  Encourage additional activities over and above table top exercise.

## Slide 4: PacWave Planning, Conduct, Evaluation
  PacWave Exercises Task Team:
  Three co-chairs
    Laura Kong - ITIC
    Jo Guard - New Zealand
    Tomoaki Ozaki - Japan
  Members - same for PacWave16 and 17
    Viviana Dionicio – Colombia
    Jun-Hee Lee – Korea
    Yuelong Miao – Australia
    Jerome Aucau – New Caledonia
    Dominique Reymond – French Polynesia
    Viacheslav Gusiakov and Tatiana Ivelskaya – Russia
    Chip McCreery – PTWC

## Slide 5: PacWave17 – Date and Purpose
Exercise Web Site: http://www.pacwave.info
Announcement: IOC CL 2636 issued 16 August 2016
  15-17 February 2017: PTWS Exercise Pacific Wave “PacWave17”
Exercise Purpose: The aim of PacWave17 is to test the NWPTAC enhanced products and PTWC enhanced products. Proposed new SCSTAC products tested in parallel with PacWave17

## Slide 6: PacWave17 – Objectives
Test communications from the PTWS PTWC and NWPTAC Tsunami Service Providers to Member States.
Test whether the PTWS PTWC and NWPTAC Tsunami Service Provider products are interpreted by Member States accurately and in a timely manner.
Test national and regional communication.
Test national and regional cooperation.

## Slide 7: PacWave17 – 7 Scenarios
All scenarios: Magnitude: M9.0
Depth 20 km (except Manila)
Manila Trench (Depth 35 km)
New Britain-San Cristobal Trench (PacWave16)
New Hebrides Trench (PacWave11)
Tonga Trench (PacWave11, 15)
Peru-Chile Trench (PacWave11)
Colombia-Ecuador Trench (PacWave11)

## Slide 8: PacWave17 – Conduct
Exercise Date:
      Event start live, but may conduct on diff date / time
      15 Feb: Colombia-Ecu, Peru-Chile, Tonga
      16 Feb: New Hebrides, San Cristobal, Manila
Exercise Type and Participants – Recommend:
      Tabletop Exercise
      Minimum participation: NTWC, NDMO
      Each Country - exercise 1 Tsunami Scenario
TSP Messages (on web site)
      PTWC, JMA NWPTAC
      Live ‘Dummy Text’ messages to start

## Slide 9: PTWC New Enhanced Products
Base threat on wave forecast models, not on pre-determined magnitude threshold
Forecasts constrained by EQ mechanism (W-CMT) and sea level readings
Public Text Msg continues – Summary Information
Graphical forecasts and Statistics table only to Country Tsunami Warning Focal Points (TWFP):
  Coastal Tsunami Amplitude Forecast Polygon Map - Overview
  Deep-Ocean Tsunami Amplitude Forecast Map – Pacific-wide
  Coastal Tsunami Amplitude Forecast Map – Pacific-wide and Regional, with Tsunami Travel Times
  Coastal Tsunami Amplitude Forecast KMZ– input to Google Earth
  Table of Forecast Statistics for Regional Polygons
Notes: Please see explanation in:
Users Guide for the Pacific Tsunami Warning Center Enhanced Products for the Pacific Tsunami Warning System. IOC Technical Series No 105, Revised edition. UNESCO/IOC, 2014 (English; Spanish)
Available for download at http://ptws-ptwcnewproducts.info
<number>

## Slide 10
No Warning / Watch Alert Levels
Instead, issue Threat Levels: 4 categories based forecast maximum coastal tsunami wave amplitudes
  < 0.3m (no Threat)
  0.3 to < 1m
  1 to 3m
  > 3m
  Other: Forecast not yet computed
PTWC New Enhanced Products
Notes: Please see explanation in:
Users Guide for the Pacific Tsunami Warning Center Enhanced Products for the Pacific Tsunami Warning System. IOC Technical Series No 105, Revised edition. UNESCO/IOC, 2014 (English; Spanish)
Available for download at http://ptws-ptwcnewproducts.info
<number>

## Slide 11: Northwest Pacific Tsunami Advisory Centre
  Developed and tested – PacWave16, 17 Implement 2018 with ICG/PTWS approval
  NWPTA Forecast Points: revised to align with PTWC products, and meet Member States requests
Text Products – continue as before
Graphical Products – sent by email
  Travel Time Map
  Coastal Tsunami Amplitude Forecast Map
  Deep-ocean Tsunami Amplitude Forecast Map
<number>

## Slide 12: NWPTA Recipient Countres, Area Coverage
NWPTA will be issued to 16 recipient countries when the NWPTAC detects occurrence of an earthquake of magnitude 6.5 or greater in the blue-shaded area.
<number>

## Slide 13: NWPTAC Products: Tsunami Travel Time
This map shows the estimated travel time based on determined earthquake location (hypocenter or centroid) and magnitude.
Uncertainties in tsunami source (the area of seafloor deformation is assumed from earthquake location and magnitude)
Uncertainties in bathymetry especially in the vicinity of the observation point
Nonlinear effects on tsunami propagation which is not taken into account in estimating travel time (the nonlinear effects may be important especially in shallow water)
Difficulty in measuring the first wave arrival from observed sea level data
JMA HPより
Limitations
Actual arrival time at the coast may vary from forecast arrival time due to many reasons including:
<number>

## Slide 14: Coastal Tsunami Amplitude Forecast
This map shows the individual coastal points colored according to the forecast tsunami amplitude at each point
The larger of two different forecast amplitudes based on a conjugate fault set obtained by CMT analysis is used as a forecast tsunami amplitude at each point
Uncertainties in tsunami source (two rectangular faults are assumed based on the result of CMT analysis)
Uncertainties in the way that the tsunami interact with the coast (a general approximation, Green’s Law, is used)
Limitations
Actual tsunami amplitudes at the coast may vary from forecast amplitudes due to many reasons including:
The results can vary easily by a factor of two because of the uncertainties written above.
<number>

## Slide 15: Deep-ocean Tsunami Amplitude Forecast
This map shows the maximum tsunami amplitude at each place in the deep ocean.
It shows how the tsunami is directed away from the tsunami source, how it is focused and defocused by the shape of the seafloor, and how it diminishes by spreading
Two different maps based on a conjugate fault set obtained by CMT analysis will be provided
Limitations
Actual deep-ocean tsunami amplitude may vary from forecast amplitudes mainly due to uncertainties in tsunami source (two rectangular faults are assumed based on the result of CMT analysis).
This map should not be used to estimate coastal tsunami amplitudes or impacts.
<number>

## Slide 16: PacWave17 - Documents
PacWave17 web site: www.pacwave.info
  Exercise Messages (PTWC, JMA/NWPTA)
  PacWave Exercise Manual (IOC TS 131, 2016)
  User’s Guide to PTWC Enhanced Products for the PTWS (IOC TS 105, revised, 2014)
  PacWave17 Summary (this ppt)
  How to Plan, Conduct, and Evaluate IOC Tsunami Wave Exercises (IOC M&G 58 2013)
  PacWave17 Announcement (IOC CL 2636, 16 Aug 2016)

## Slide 17: PacWave17 - Evaluation
Post-Exercise Evaluation
  Due 10 March 2017
  Preliminary Results available for ICG/PTWS-XXVII, 28-31 March 2017
  Online: https://www.surveymonkey.com/s/pacwave17_eval

## Slide 18: PacWave17 Timetable
4 Nov 2016 | Nominate PacWave17 National Contact
1 Dec 2016 | Exercise manual (incl scenarios) on www.pacwave.info
31 Jan 2017 | Exercise messages posted
15-17 Feb 2017 | PacWave17
18 Feb -10 Mar 2017 | Countries complete and submit evaluation survey online
28 - 31 Mar 2017 | Draft Preliminary Results discussed at ICG/PTWS-XXVII
21 Apr 2017 | Draft PacWave17 Preliminary Report available to Member States
30 Jun 2017 | Final PacWave17 Summary Report on www.pacwave.info

## Slide 19: Exercise Pacific Wave, 2006-2016: A decade of reflection
Notes: <number>

## Slide 20: PacWave6: 16-17 May 2006
Exercise Purpose: To test, exercise, evaluate and review the operational lines of communication within the Pacific Tsunami Warning and Mitigation System’s area of responsibility
Participants: 44 countries
Scenarios: 1
Notes: <number>

## Slide 21: PacWave6: Objectives
Validate the Tsunami Warning Centres’ dissemination process of issuing tsunami watch and warning bulletins to Pacific basin countries;
Validate the process for countries to receive and confirm tsunami bulletins;
Validate dissemination of warning messages to relevant agencies within a country, provinces and local jurisdictions;
Validate the organisational decision making process about public warnings and evacuations;
Identify the modes that would be employed to notify and instruct the public; and
Assess the elapsed time until the public would be notified and instructed.
Notes: <number>

## Slide 22: PacWave8: 28-30 October 2008
Exercise Purpose: The purpose of the exercise was to evaluate and improve the effectiveness of the PTWS, its operational Tsunami Warning Centers, and its Member States in responding to a destructive tsunami.
Participants: 40 countries
Scenarios: 1
Notes: <number>

## Slide 23: PacWave8: Objectives
Validate the international Tsunami Warning [or Advisory] Centers’ dissemination process of issuing Tsunami Watch and Warning Bulletins to Pacific countries;
Validate the process of countries receiving and confirming Tsunami Bulletins through their designated focal point;
Validate dissemination of warning messages to relevant agencies within a country;
Validate the organizational decision making process about public warnings and evacuations;
Identify the methods that would be used to notify and instruct the public;
Assess the elapsed time until the public would be notified and instructed.
Notes: <number>

## Slide 24: Real Tsunami events: 2009-2011
M8.0 Samoa - 29 September 2009
  Samoa – 149 deaths, -20% GDP impact
  American Samoa – 34 deaths, $90 million damage
  Niuatoputapu Island, Tonga – 9 deaths, airport inoperable (debris), so at 1st only ship access
M8.8 Chile – 27 February 2010
  156 deaths, $600 million damage
  Civil court cases (ONEMI, SHOA liable)
M9.0 Japan – 11 March 2011
  ~18,000 dead or missing, $6 billion damage
  Civil court cases (Ishinomaki, school liable, 74 school-children died)
Notes: <number>

## Slide 25: Improving Exercise Conduct
How to Plan, Conduct and Evaluate UNESCO/IOC Tsunami Wave Exercises (IOC, Manual & Guides 58, 2013, English, Spanish)
NZ Ministry of Civil Defence and Emergency Management, ITIC collaboration
Draft used PacWave11
Notes: <number>

## Slide 26: PacWave11: 9-10 November 2011
Exercise Purpose: To improve local and regional source tsunami warning and response capability in the Pacific.
Participants: 35 countries
Scenarios: 10
Notes: <number>

## Slide 27: PacWave11: Objectives
To exercise and evaluate operations of the current PTWS, including:
    Validate the issuance of tsunami advice from PTWC, JMA/NWPTAC and WCATWC
    Validate receipt of this tsunami advice by Pacific Country TWFP
To begin a process of exposure to an initial test version of PTWC experimental products that were being developed to provide a more rapid and quantitative forecast of tsunami impacts:
    Review and evaluate PTWC experimental products that will be available in parallel with existing PTWC products for each scenario exercised.
    Provide feedback on the staging, format, and content of the experimental products.
To validate the readiness of Member States to respond to a local/regional source tsunami:
    Validate the operational readiness of the National Tsunami Warning Centre (NTWC), or similar in-country function, and/or the National Disaster Management Office (NDMO).
    Improve operational readiness. Before the exercise, ensure
    appropriate tools and response plan(s) have been developed,
    including public education materials.
    Validate dissemination of warnings and information/advice by
    NTWC to relevant in-country agencies and the public is accurate and timely.
    Validate the organisational decision-making process about public warnings and evacuations.
    Validate the methods used to notify and instruct the public are accurate and timely.

## Slide 28: PacWave13: 1-14 May 2013
Exercise Purpose: The aim of PacWave13 is to validate the understanding and use of the PTWC Enhanced Products.
  Evaluate the format and content of the PTWC Enhanced Products for each scenario exercised
  Provide feedback that a country is prepared to officially receive and implement and utilize the PTWC Enhanced Products
  Provide feedback that a country’s stakeholder agencies will be informed on the PTWC Enhanced Products so as to make appropriate future changes to their Standard Operating Procedures.
Participants: 34 countries
Scenarios: 3
Notes: <number>

## Slide 29: PacWave15: 2-6 February 2015
Exercise Purpose: To test the new PTWC Enhanced Products
Test communications from the PTWS Tsunami Service Providers to Countries.
Test whether the PTWS PTWC Tsunami Service Provider products are interpreted by countries accurately and in a timely manner.
Test national and regional cooperation.
Participants: 41 countries
Scenarios: 6
Notes: <number>

## Slide 30: PacWave15 - Evaluation Summary
Majority received messages in timely manner without issues.
Majority ranked the text message as most useful product
KMZ file least useful product
Format and content of products clear and easy to interpret
Respondents understand the contents of the enhanced products
Information provided assists with decision making
<number>
Notes: <number>

## Slide 31: PacWave15 - Evaluation Summary
Countries open to receiving higher resolution products
NTWC/NDMOs have activation and response processes
Respondents used national tsunami experts to help assess threat messages
40% of respondents have tsunami related curriculum programmes in all levels of education
Stakeholder agencies have a better understanding of their goals, responsibilities and roles in tsunami emergencies.
<number>
Notes: <number>

## Slide 32
Tsunami Warning Focal Point contact data
Issue: TWFP contact information needs to be 100% accurate 100% of the time
Recommendation: Countries to routinely review contact information, inform IOC (who will then forward to Tsunami Service Providers)
<number>
PacWave15 - Recommendations
Notes: <number>

## Slide 33: PacWave15 - Recommendations
Exercise Planning
Issue: Insufficient time provided to fully prepare for the exercise
Recommendation:
IOC to announce future PacWave activities at least 6 months prior
Exercise manual to be published 3 months prior
Tsunami Service Providers to provide products at least 1 month prior.
<number>
Notes: <number>

## Slide 34
Community Preparedness
Issue: 35% of countries do not have evacuation maps, signs, routes, assembly areas etc. This hampers a community to plan for tsunami response.
Recommendation:
IOC and Member States should support preparedness efforts as highest priority.
All communities should have tsunami evacuation maps
<number>
PacWave15 - Recommendations
Notes: <number>

## Slide 35
Routine exercising
Issue: 35% of countries do not conduct annual, routine tsunami exercises.
Recommendation: Countries are encouraged to conduct annual tsunami exercises (starting with small, controllable coastal school drills).
<number>
PacWave15 - Recommendations
Notes: <number>

## Slide 36
Conduct of future exercises
Issue: Past PacWave exercises have been conducted in controlled, moderately-paced timelines, in a table-top format. Many countries are now ready to move towards more realistic exercise response timeline.
Recommendation: Future PacWave exercises should be conducted in real time, initially during the daytime working hours with full staffing. Later, consideration should be given to real time exercises simulating minimal staff during night time or weekend hours.
<number>
PacWave15 - Recommendations
Notes: <number>

## Slide 37: PacWave16: 1-5 February 2016
Exercise Purpose:
The aim of PacWave16 is to evaluate experimental NWPTAC Enhanced Products and identify necessary modifications.
Evaluate the format and content of experimental NWPTAC Enhanced Products.
Determine whether countries are prepared to officially receive and utilize the NWPTAC Enhanced Products.
Participants: 12 countries
Scenarios: 6

## Slide 38: Thank You
Dr. Laura Kong, ITIC
laura.kong@noaa.gov
Jo Guard, MCDEM
jo.guard@dpmc.govt.nz
Tomoaki Ozaki, JMA
tozaki@met.kishou.go.jp
Notes: <number>